## Slide 1: Characterizing Error in Linear Battery State of Charge Model CEE 292X Fall 2019 Corey Shono & Timnah Zimet
Methodology
Linear SOC estimation with constant efficiency coefficient
As a “ground truth” we use the simulation results of the BDS default NiMH cell ECM. We then compare the simulation SOC to the results using the following simple model:
where Q is the state of charge, c is the charge rate, d is the discharge rate, ϒc and ϒd are the charge and discharge efficiencies, and Δt is the time step.
To calculate ϒc and ϒd, we use a pulse cycle in BDS, so that c and d are each constant for long time periods.
To evaluate the accuracy, we then use these ϒc and ϒd to predict the SOC with realistic charge cycles, and compare to the BDS results with the same cycles.
The accuracy is measured as residuals, or error in % SOC, at each time step. Error accumulates at each time step, so the final residual value is a good indicator of accuracy for the time period.
Additional battery modeling in literature
Existing literature mostly focuses on a constant efficiency term that affects the resistive component of an ECM, or assumes the constant efficiency we analyze here in order to do other experiments. One exception is a mathematical model with piecewise efficiency terms [1].
Results
Acknowledgements
Thank you to our mentor, Thomas Navidi.
Conclusions & Future Work
Key takeaways
In more smooth/regular cycles, the absolute error in SOC due to efficiency approximation is less than 1%.
In cycles with higher variation, the absolute error in SOC increases.
The actual error in real measurements is a result of noise and inaccurate current measurements, in addition to SOC estimation.
Future steps
Evaluate additional models for efficiency as a function of temperature, SOC, etc.
Observe effects on entire battery pack as opposed to single cell.
Observe accuracy for transportation battery cycles.
Background
Battery state of charge (SOC) cannot be measured directly in practice, and yet it is important in all battery applications. While complex models of batteries and equivalent circuit models (ECMs) offer more accurate results, mathematical approximations are used often. The simplest approximation is efficiency as a constant coefficient of charge.
Key Questions
How accurate is the approximation of a constant efficiency as the coefficient of charge or discharge current?
Are other simple mathematical models of efficiency able to better approximate the battery SOC?
Bibliography
[1] N. DiOrio, A. Dobos, S. Janzou, A. Nelson, and B. Lundstrom, “Technoeconomic Modeling of Battery Energy Storage in SAM”, National Renewable Energy Laboratory, Tech. Report. TP-6A20-64641, Sep. 2015.
[2] W. Powell and H. Cheng. Workshop, “Co-optimization of battery storage over multiple revenue streams and time scales.” PENSA Laboratory, Princeton University, Princeton, NJ, Jun. 21, 2015.
[3] E. Raszmann, K. Baker, Y. Shi, and D. Christensen, “Modeling Stationary Lithium-Ion Batteries for Optimization and Predictive Control” National Renewable Energy Laboratory, Tech. Report. CP-5D00-67809, Feb. 2017.
Calculating efficiency terms
Input cycle:
1A charge and discharge rates at 1 hour each
Results:
Charge efficiency: 0.9889
Discharge efficiency: 0.9988
(or 1.001178 in SOC equation)
Evaluating accuracy: compare BDS to linear efficiency SOC prediction
Input cycle: daily peak shifting
Results: Max residual 0.078% SOC, final residual 0.055% SOC
Input cycle: regulation D signal
Results: Max residual -0.16% SOC, final residual -0.065% SOC
Input cycle: less smooth regulation D signal
Results: Max residual 4.1% SOC, final residual 1.2% SOC
Motivation