## Slide 1: Characterizing Error in Linear Battery State of Charge Model CEE 292X Fall 2019 Corey Shono & Timnah Zimet
Methodology
Linear SOC estimation with constant efficiency coefficient
As a “ground truth” we use the simulation results of the BDS default NiMH cell ECM. We then compare the simulation SOC to the results using the following simple model:
where Q is the state of charge, c is the charge rate, d is the discharge rate, ϒc and ϒd are the charge and discharge efficiencies, and Δt is the time step.
To calculate ϒc and ϒd, we use a pulse cycle in BDS, so that c and d are each constant for long time periods.
To evaluate the accuracy, we then use these ϒc and ϒd to predict the SOC with realistic charge cycles, and compare to the BDS results with the same cycles.
The accuracy is measured as residuals, or error in % SOC, at each time step. Error accumulates at each time step, so the final residual value is a good indicator of accuracy for the time period.
SOC estimation with variable efficiency
In order to capture the effects of SOC and charge rate on the battery’s internal resistance, a multivariate linear model was fitted to predict the efficiency of each timestep for a given SOC and current according to the following equation:
SOC is then predicted in the same forward-stepping fashion as before from t=0 but with efficiency updated at each time step. The residuals over time were compared between the two models
Additional battery modeling in literature
Existing literature mostly focuses on a constant efficiency term that affects the resistive component of an ECM, or assumes the constant efficiency we analyze here in order to do other experiments. One exception is a mathematical model with piecewise efficiency terms [1].
Results
Acknowledgements
Thank you to our mentor, Thomas Navidi.
Conclusions & Future Work
Key takeaways
Fixed efficiency SOC predictions perform better on the unseen test cycle that spans similar SOC’s to the training cycle.
Training variable efficiency models on cycles with a significant amount of variability in SOC and charge rate provides better SOC estimation on unseen test signals.
SOC predictions using a variable efficiency term as a function of SOC and current provides less drift in residuals over time than the predicting based on the average efficiency
Higher measurement error negates the improved performance of the variable efficiency model
Future steps
Perform cross-validation using more than 1 signal to train the model
Incorporate temperature effects into the variable efficiency model
Observe accuracy for transportation battery cycles.
Assess impacts of uncertainty on optimal control
Background
Battery state of charge (SOC) cannot be measured directly in practice, and yet it is important in all battery applications. While complex models of batteries and equivalent circuit models (ECMs) offer more accurate results, mathematical approximations are used often. The simplest approximation is efficiency as a constant coefficient of charge.
Key Questions
How accurate is the approximation of a constant efficiency as the coefficient of charge or discharge current?
Are other simple mathematical models of efficiency able to better approximate the battery SOC?
Bibliography
[1] N. DiOrio, A. Dobos, S. Janzou, A. Nelson, and B. Lundstrom, “Technoeconomic Modeling of Battery Energy Storage in SAM”, National Renewable Energy Laboratory, Tech. Report. TP-6A20-64641, Sep. 2015.
[2] W. Powell and H. Cheng. Workshop, “Co-optimization of battery storage over multiple revenue streams and time scales.” PENSA Laboratory, Princeton University, Princeton, NJ, Jun. 21, 2015.
[3] E. Raszmann, K. Baker, Y. Shi, and D. Christensen, “Modeling Stationary Lithium-Ion Batteries for Optimization and Predictive Control” National Renewable Energy Laboratory, Tech. Report. CP-5D00-67809, Feb. 2017.
Calculating Fixed Efficiency Terms: Fit efficiency on a simple 1A cycle
Input cycle:
1A charge and discharge rates at 1 hour each
Results:
Charge efficiency: 0.9889
Discharge efficiency: 0.9988
(or 1.001178 in SOC equation)
Fixed Efficiency SOC Prediction: Characterize residuals on regulation D signals
Motivation
Std Dev (Amps) | Max Current (Amps) | Number of Signals
5 | ± 40 | 8
15 | ± 40 | 7
25 | ± 40 | 3
30 | ± 40 | 4
Training cycle: Current randomly sampled every 10 min from (0, 25) capped at ±40 Amps for 10 hrs.
Test cycles: 0 mean random-normal signal according to the table below:
10-bit Measurement Error (0.1% full span)
12-bit Measurement Error (0.024% full span)
Distribution of Residuals on 20 Random Test Cycles
Test Cycle | Max Residual | Final Residual
Regulation D Signal 1 | -0.16 % SOC | -0.065% SOC
Regulation D Signal 2 | 4.1% SOC | 1.2% SOC
RegD Test Cycles
Residual Distribution and Time Evolution
Variable Efficiency: Compare residuals using variable vs. fixed efficiency prediction
Experimental Current Measurement Error: Compare residuals for different levels of error